## Slide 1: Internet of Things Requirements and solutions

## Slide 2: Agenda
IoT and M2M
Prospects
Requirements
Challenges
Solutions
Conclusions and discussion

## Slide 3: IoT and M2M
Smart, connected devices
Collecting and exchanging data autonomously
Little or none human intervention

## Slide 5: Prospects
2014 - Cisco
2015 - Ericsson

## Slide 6: Drivers
Diminishing prices for devices
Diminishing costs for data plans
Barriers
Security & privacy
Large number of devices
Various (small) packet sizes
Various latency & reliability requirements
Billing

## Slide 7: Requirements
Packet size
Packet arrival rate
Maximum latency
Energy efficiency
Reliability

## Slide 8: Challenges
Interference (unlicensed spectrum)
Delay – for CSMA-CA or due to collisions
Scheduled transmissions -> overhead
  H2H LTE ~ 25 % overhead
  NB-LTE ??
Non-scheduled -> Collisions
  100 users x 10,000 KB ≠ 10,000 users x 100 KB
2015 Semester project – group 850 WCS

## Slide 9: Solutions
Re-engineering
  GSM
  UMTS
  LTE (NB-LTE)
New protocols
  Sigfox
  LoRa
  Weightless
  Wi-Fi 802.11ah
  Ingenu RPMA
“Old” protocols
  Bluetooth
  ZigBee

## Slide 10: GSM for M2M
Frequencies (licensed) – 850, 900 MHz preferred
GMSK modulation – low complexity PA
Data rate – 9.6 Kbps
Multiple access
  FDMA – 125 channels
  TDMA – 8 slots
  Slotted random access
    217 RACH/s
    24 AGCH/s (enhanced to 24 x 4)

## Slide 11: NB-LTE
Scheduled access – good or bad
Licensed frequency spectrum
64 preambles for random access
Preventing overload
  Separate RACH resources for M2M and H2H
180 KHz UL & DL (SC-FDMA )

## Slide 12: Sigfox
Sub 1-GHz unlicensed spectrum
Ultra narrow band + continuous frequency hopping
Range: 10 km urban / 50 km rural
Uplink: 100bps, 12 bytes/message, 140 messages/day
1 million devices per base-station
Base-stations 1000 times more efficient than GSM
3 msg/day & 2.5Ah battery => 20 years autonomy

## Slide 13: LoRa
Sub 1-GHz unlicensed spectrum
125 KHz channels (8 in Europe, 64 in US)
Data rate – 50 kbps
Unlimited packets/day and up to 255 bytes/packet
Range: 5 km urban / 15 km rural
Over 1 million devices / base-station

## Slide 14: Weightless
Little overhead
Weightless –N:
  Narrowband, 200 Hz channels, unlicensed sub 1-GHz
  Frequency hopping
  Uplink only, 100 bps
  Range: 3 km urban
Weighless –W: white space TV frequency (400-800 MHz)
  UL & DL (TDD)
  5 MHz channel, 10 Mbps

## Slide 15: Wi-Fi 802.11ah
Unlicensed sub 1-GHz ISM spectrum
“Long range Wi-Fi” – up to 1.5 km rural
Channels: 1, 2, 4, 8, 16 MHz (Europe ISM band size ~ 6 MHz)
Restricted access window (RAW)
CSMA-CA
UL & DL
Up to 8000
devices

## Slide 16: Others
Bluetooth & ZigBee
  Short range
  Cheap
Ingenu RPMA
  2.4 GHz unlicensed band
  “Carefully synchronized”
  Signaling and power control required

## Slide 17: Conclusions & Discussion
What to choose:
Unlicensed vs. licensed spectrum
Scheduled vs. random access
Range vs. power consumption
Many solutions, limited spectrum – what about interference